## Slide 1: Frequency Shift Keying (FSK)
Duncan Wood
ENCE 4110
11/12/2025

## Slide 2: Introduction
Problem: Convert UART data into modulated FSK signal and send it back to the PC demodulated
MODULATOR
DEMODULATOR

## Slide 3: What is Frequency Shift Keying?
FSK is a digital modulation technique widely used in modern technology.
Bluetooth, digital radios, remotes.
The digital counterpart of Frequency Modulation (FM)

## Slide 4: In this system...

## Slide 5: System Overview
PC
SERIAL
UART
RX
FSK
TX
FSK MOD
FSK
DEMOD
UART
TX
PC
SERIAL
7-SEG
SCOPE
HEX[0]
GPIO[0]
BYTE
ASCII CHAR

## Slide 6: FSK Transmit FSM
Serializes byte into 10-bit frame (start, data, stop)
Holds each bit for defined number of clock cycles; the symbol period.
Synchronizes the UART data with the FSK modulator.
IDLE
LOAD
SEND
Data ready
recorded
Sent to modulator

## Slide 7: Symbol Timing
UART Baud: 115200
FPGA Clock: 50 MHz
Clocks per symbol = 50e6 / 115200 ≈ 434
One bit = 434 clock cycles → one full tone interval

## Slide 8: FSK Modulator
Simple toggle-counter structure:
  Counter resets when reaching N₀/N₁
  Output bit flips on reset → square wave
Frequency
  f=1/(2xN)
  If bit==1 use N1 (shorter interval → higher frequency).
  If bit==0 use N0 (longer interval → lower frequency).
FSM
Single bit
Toggle
Select
N0/N1
counter
Toggle FSK Signal
counter++ / clk

## Slide 9: FSK Demodulator
Edge-counting demodulator:
  Detect transitions of fsk_in
  Count edges per symbol window (434 clocks)
  Compare to threshold (~20 edges)
Decision rule:
  More edges → high tone → bit = 1
  Fewer edges → low tone → bit = 0
Reassemble bits into bytes
MOD
FSK Signal
Edge detector
Symbol timer
Increments edge counter
Cycles clk until symbol period reached
Sample
Recovered byte

## Slide 10: UART Transmitter / Receiver
PC
SERIAL
UART
RX
UART
TX
PC
SERIAL
FSK
Receive and transmit the input and output message of the FSK logic.

## Slide 11: Testing and Verification

## Slide 14: Future Work
Problem Observed
Characters echoed from the demodulator do not match the UART key pressed
Indicates bit or symbol misalignment between transmitter and receiver timing.
Likely causes
Symbol boundary drift — demodulator’s 434-clock window may start mid-symbol
Threshold sensitivity — fixed midpoint (≈ 20 edges) may mis-classify noisy or marginal tones.
Byte framing ambiguity — demodulator doesn’t yet detect start/stop bits; it simply groups 8 bits sequentially.
Possible Solution: add protocol layer and additional synchronizer to implement start/stop validation.

## Slide 15: Conclusions
Built a complete digital FSK modem on FPGA.
.Demonstrated real-time chain:
  UART RX → FSK TX FSM → Modulator → Demodulator → UART TX
Key Insights
Timing precision is key for symbol alignment
Simple edge count demodulation works conceptually but lacks robustness.